## Slide 1: Generating velocity solutions with globk
M. Floyd K. Palamartchouk
Massachusetts Institute of Technology Newcastle University
GAMIT-GLOBK course University of Bristol, UK 12–16 January 2015
Material from R. King, T. Herring, M. Floyd (MIT) and S. McClusky (now ANU)

## Slide 2: GLOBK Velocity Solutions
The aim of these solutions is to combined many years of data to generate position, velocity, offset, and postseismic parameter estimates. Not uncommon to have 10000 parameters in these solutions.
Input requirements for these solutions:
  Apriori coordinate and velocity file. Used as a check on positions in daily solutions (for editing of bad solutions) and adjustments are apriori values (apriori sigmas are for these values)
  Earthquake file which specifies when earthquakes, discontinuities, and mis-named stations affect solution. Critical that this file correctly describe data.
  Process noise parameters for each station. Critical for generating realistic standard deviations for the velocity estimates.

## Slide 3: Velocity Solution Strategies
In general careful setup (i.e., correct apriori coordinate, earthquake file and process noise files) is needed since each run that corrects a problem can take several days. In correct solutions may not complete correctly.
Previous methods for constructing these solutions:
  Define a core-set of sites (usually 20-200 sites) where the solution runs quickly. Test files on this solutions and use the coordinate/velocity estimates to form the reference frame for time series generation.
  Time series using these reference frame sites and then test (RMS scatter, discontinuity tests) to form a more complete earthquake and apriori coordinate/velocity files.
  Steps above are repeated, usually increasing number of stations until solution is complete. As new stations are added missed discontinuities and bad process noise models can cause problems.

## Slide 4: Velocity strategies
Other methods that are used to increase speed are:
  Pre-combine daily solutions into weekly to monthly solutions and use these combined solutions in the velocity solutions. There are many advantages to this approach:
    Runs are much faster. Each processing step takes about the same time with the monthly as a daily file but there are 30 fewer files so 30 times faster.
    Numerical rounding errors are much better when monthlies are used
    New MIDP output option refers the solutions to the middle of the month. (Earlier versions used last day of month as reference time, natural time for a sequential Kalman filter.
    Random walk process noise models correct when velocity NOT estimated in combinations
  Run decimated solutions (e.g., one day per week). Works fine and changing start day does not have large effect due to correlated noise models. Care needed when different start day results are combined to avoid white noise sigma reduction.

## Slide 5: Before velocity runs
Surveys may be combined into one solution per survey
No need to re-run glred again to see long-term time series
Multiple “.org”-files may be read by tssum or sh_plot_pos
  tssum pos mit.final_igb08 -R survey1_comb.org survey2_comb.org ...
  sh_plot_pos -f survey1_comb.org survey2_comb.org -k ...

## Slide 6: Long-term time series
Reasonable repeatability
Outlier in vertical

## Slide 7: Excluding outliers or segments of data
Create “rename” file records and add to GLOBK command file’s “eq_file” option, e.g.
  rename PTRB PTRB_XPS h1407080610_nb4a
  rename PTRB PTRB_XPS 2014 07 07 18 00 2014 07 08 18 30
  rename ABCD ABCD_XCL 2013 07 08 00 00
“XPS” will not exclude data from glred (so still visible in time series) but will exclude data from globk (combination or velocity solution)
“XCL” will exclude data from all glred or globk runs

## Slide 8: Run globk
Create new “.gdl”-file with combined binary h-files, e.g. from vsoln/, assuming standard directory hierarchy
  ls ../*/gsoln/*.GLX > vsoln.glx.gdl
Optionally run glist again
  Recommended to prevent problems during long globk run
Run globk
  This may take many hours for very large/long velocity solutions

## Slide 9: glorg for different reference frames
No need to re-run globk every time you want
glorg is usually called from globk command file (“org_cmd” option) but glorg may be run separately
globk 6 globk_vel.prt globk_vel.log globk_vel.gdl globk_vel.cmd
glorg globk_vel_noam.org ERAS:… glorg_vel.cmd vel.com
Must have saved the “.com”-file!
  e.g. “com_file @.com”
  Do not use “del_scra yes” in globk command file