## Slide 1: Examples of track use
M. Floyd K. Palamartchouk
Massachusetts Institute of Technology Newcastle University
GAMIT-GLOBK course University of Bristol, UK 12–16 January 2015
Material from R. King, T. Herring, M. Floyd (MIT) and S. McClusky (now ANU)

## Slide 2: Outline
Kinematic examples
  GPS seismology
  Roving GPS
  Rapid deformation
Static examples
  Short-static occupations
  Deciphering interference
Remember the rule-of-thumb for proportional errors:
  εBL ~ εSV × BL/hSV

## Slide 3: Example 1: GPS seismology
Examine the short baseline MIT results: Look at this example in more detail later
April 4, 2010 El-Mayor Cucapah earthquake in Baja California: 5-Hz results. Look later at long baseline processing for these sites.
Track results are generated in two steps:
  First solution uses zero process noise except during time of earthquake (long baseline solution)
  Final results generated with fixed ambiguities from first solution read in (-a option).
  Long baseline ambiguity resolution with stochastic site coordinates needs LC estimate which can noisy due to stochastics.

## Slide 4: Coseismic offsets
Offsets based on 2-days before and after earthquake.
Two days used is reduce leakage of postseismic motions.
Red Star is epicenter; blue circle is 60 km (15-20 seconds surface wave speed)

## Slide 5: Zoom around border
Sites near the epicenter.
Blue circle is 60 km radius
Displacements P494 200 mm P496 182 mm P497 97 mm … P491 9 mm

## Slide 6: High-rate GPS site download
High rate data from these sites downloaded after event.
Most sites are 5-Hz; more distant sites are 1-Hz.
Reference site for high rate positioning
1Hz reference site

## Slide 7: Sites in coseismic region
Sites shown have 5-Hz data for 3-days before and after the earthquake
Examine sequence of sites along US/Mexico border and North
Notes: P494, P496 P500 P066 P473 P472 sequence in next slides.

## Slide 8: P496

## Slide 9: P494

## Slide 10: P500

## Slide 11: P066

## Slide 12: P473
Notes: Note that this and the next site are similar distances from the epicenter but P742 is along the San Andreas. Also point out the 220-sec arrival

## Slide 13: P742

## Slide 14: Surface wave arrival at P725
P725 is ~600 km from epicenter. This signal common to sites is the arrival at the “reference site”
Notes: Low rate data from distance reference site (with sign flipped)

## Slide 15: Example 2: Roving GPS (from England et al., 2013)
Disclaimer: This example was not processed using TRACK because the kinematic equipment was single-frequency, i.e. L1-only, and TRACK requires dual-frequency data
Notes: Roving GPS profiles traversing lake terraces allow us to determine the height and position of paleo-shorelines, here around lakes in southern Tibet (England et al., 2013). Static base stations are seen as triangles marked “BSnn”. The GPS receiver was left on while driving between localities in the field area (note 22.5 km scale bar in bottom left corner of left-hand figure), hence the long tracks (coloured by elevation). Specific high-resolution profiles and were taken on foot at many tens of locations, such as those seen in the right-hand figures. Ellipsoid heights converted to geoid heights using EGM2008 model (Pavlis et al., 2012).

## Slide 16: Example 3: Rapid deformation (from Ryder et al., 2012)
Two earthquakes within 15 minutes of one another
InSAR shows cumulative deformation but no way to separate events
Epoch-by-epoch (rather than batch) GPS processing may help...
Ryder et al. (2012), Figure 1
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 17: Example 3: First run
Key TRACK commands:
site_stats
iloc 0.5 0.5 0.5 0 0 0
lemu 0.5 0.5 0.5 0 0 0
navi 0.5 0.5 0.5 0 0 0
timedep_procns
iloc 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
lemu 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
navi 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
iloc 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
lemu 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
navi 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
Second run (updated apr):
site_stats
iloc 0.02 0.02 0.02 0 0 0
lemu 0.02 0.02 0.02 0 0 0
navi 0.02 0.02 0.02 0 0 0
timedep_procns
iloc 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
lemu 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
navi 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
iloc 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
lemu 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
navi 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
site_pos ...
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 18: Example 3: Final run
Key TRACK commands:
site_stats
iloc 0.02 0.02 0.02 1 1 1
lemu 0.02 0.02 0.02 1 1 1
navi 0.02 0.02 0.02 1 1 1
#timedep_procns
# iloc 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
# lemu 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
# navi 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00
# iloc 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
# lemu 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
# navi 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
ambin_file
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 19: Example 4: Short-static occupations
Short spans of data (e.g. 30 minutes) may be processed with GAMIT
Risk of all data being removed during cleaning (AUTCLN) if not high quality
TRACK may be used in “short-static” approach with fixed, continuously recording and well positioned base site
Long session base site with accurate a priori coordinate calculated using GAMIT
Rover
Rover
Rover
Rover

## Slide 20: Example 4: Short-static occupations
Notes: Data from 2000 and 2001 are short-static occupations processed with track. All other data are regular geodetic occupations processed with GAMIT. Note the large outlier (incorrect ambiguity resolution?) at B245 in 2001.

## Slide 21
Sometimes, this happens…
1.2810 m
N
Photographs courtesy of Gareth Funning (University of California, Riverside)
Notes: Photographs courtesy of Gareth Funning (University of California, Riverside)

## Slide 22: Example 5: Deciphering interference
First TRACK run with
Re-run teqc with “-e” option to truncate RINEX file at epoch of disturbance so as not to propagate bad data
19:36
local time
Setup
Notes: The tripod at the site pictured in the previous slide (6908, off I-680 south of Cordelia, CA) appears to have been knocked over or collapsed after 2014-08-25T02:36:30Z. This still leaves ~ 5 hours of “untouched” GPS data available for regular static processing, but anything after this epoch ideally should be discarded by truncating the RINEX file to avoid propagation of unusable data.

## Slide 23: Example 5: A complex example
20:34
local time
1.0450 m
07:21
local time
~ 9 hrs
???
Notes: This site, 04LF, is within Maxwell Farms Regional Park in Sonoma, California. The path to the right (east) of the site is used as a waiting area for children attending the local school when they get on or off the school bus at the stop in the background. This site is very exposed to public interference and the example here shows how, after 03:34:00 UTC (20:34:00 local time) on 2014-08-31, the site was disturbed. Apparently it is lying on the ground (du = ~ antenna height) a few m away from the mark. Then, after 14:21:30 UTC (07:21:30 local time) the next day, it is approximately (but not exactly) replaced over the mark. Ground truth measurements were taken when the antenna was retrieved showing the replaced tripod to be ~ 70 mm away from the mark on true azimuth ~ 050° at a height of 1.0063 m, 38.7 mm lower than before. While this data may be used with the ground-truthed differential position, it is safest to truncate the data (e.g. in the RINEX file) at 2014-08-31T03:34:00Z.

## Slide 24: sh_plot_track
Reads track “NEU”, “DHU” or “XYZ” output file
May add plot to view evolution of atmospheric delay

## Slide 25: sh_kml
Script for converting several formats of result into KML format for viewing in Google Earth
  glist (may also be used with time slider)
  “.org”-file / “.vel”-file
  track “GEOD”-format output file

## Slide 26: References
England, P. C., R. T. Walker, B. Fu and M. A. Floyd (2013), A bound on the viscosity of the Tibetan crust from the horizontality of palaeolake shorelines, Earth Planet. Sci. Lett., 375, 44–56, doi:10.1016/j.epsl.2013.05.001
Ryder, I., A. Rietbrock, K. Kelson, R. Bürgmann, M. Floyd, A. Socquet, C. Vigny and D. Carrizo (2012), Large extensional aftershocks in the continental forearc triggered by the 2010 Maule earthquake, Chile, Geophys. J. Int., 188, 879–890, doi:10.1111/j.1365-246X.2011.05321.x

## Slide 27: goo.gl/CoqQZ0