## Slide 1: GPS data from receiver to processing input
M. A. Floyd T. A. Herring
Massachusetts Institute of Technology
GAMIT/GLOBK/TRACK Short Course for GPS Data Analysis
Korea Institute of Geoscience and Mineral Resources (KIGAM) Daejeon, Republic of Korea
23–27 May 2016
Material from T. A. Herring, R. W. King, M. A. Floyd (MIT) and S. C. McClusky (now ANU)

## Slide 2: Raw data formats
Receiver:
Raw format:
GPS antenna
RINEX file
Pre-processing:
Ashtech
Leica
Topcon
Trimble
B-file
R-file
.R00
.T02
.T01
.T00
Translation:
runpkr00
TEQC
RINEX Converter*
ConvertToRINEX*
* Windows only
.DAT
Notes: Different manufacturers have proprietary formats of raw data. These formats may even differ from receiver model to receiver model within a manufacturer as technology develops. We require a standardized format with which to exchange GPS data.

## Slide 3: Motivation for Receiver INdependent EXchange (RINEX) format
All manufacturers have developed their own proprietary file formats for data storage specific to their receivers and processing software
  Problems occur when processing data from another manufacturer’s receiver
RINEX developed by the Astronomical Institute of the University of Berne to allow easy and universal exchange of raw GPS data
  Principal driver was the large European GPS campaign EUREF 89 - involved more than 60 GPS receivers of 4 different manufacturers.

## Slide 4: RINEX formats
RINEX 2
  Short file names (explained in proceeding slides)
RINEX 3
  Long file names (explained in proceeding slides)
GAMIT currently works with the RINEX 2 format and GPS observables only
Support for RINEX 3 and GNSS (e.g. GLONASS) observables are under development

## Slide 5: RINEX (2) data format
Includes text file formats for:
  observation (“o”)
  navigation (“n”)
  meteorological (“m”)
  ionospheric data (“i”)
Latest definition at ftp://ftp.igs.org/pub/data/format/rinex211.txt
Each file type consists of a header section and a data section
Header section contains global information for the entire file and is placed at the beginning of the file.
  Contains header labels in columns 61-80 for each line contained in the header section
  These labels are mandatory and must appear exactly as per format description
RINEX 2 filename convention:
  For site SSSS, on day-of-year DDD, session T and year YY:
    SSSSDDDT.YYo (RINEX observation file ie the site’s GPS data)
    SSSSDDDT.YYn (RINEX navigation file ie the broadcast ephem)
  E.g., hers1270.03o is observation data for Herstmonceux, day 127, session 0, year 2003.
All the dates and times in GPST
} most important for most users

## Slide 6: An example of RINEX (2) observation data
2 OBSERVATION DATA RINEX VERSION / TYPE
National GPS Network Ordnance Survey Oct 3 01:25:41 2002PGM / RUN BY / DATE
Active Station at Ordnance Survey Office Taunton COMMENT
TAUN MARKER NAME
TAUN MARKER NUMBER
National GPS Network Ordnance Survey OBSERVER / AGENCY
0080148 LEICA RS500 0080148 REC # / TYPE / VERS
348 LEIAT504 LEIS ANT # / TYPE
The following coordinates are NOT APPROXIMATE COMMENT
Approx coords replaced by official precise ETRS89 values COMMENT
4015122.7250 -217716.1877 4934473.1877 APPROX POSITION XYZ
0.0000 0.0000 0.0000 ANTENNA: DELTA H/E/N
1 1 WAVELENGTH FACT L1/2
4 L1 C1 L2 P2 # / TYPES OF OBSERV
2002 10 3 0 0 15.000000 TIME OF FIRST OBS
2002 10 3 1 0 0.000000 TIME OF LAST OBS
END OF HEADER
02 10 3 00 00 15.0000000 0 9 2 3 8 15 17 18 22 27 31
114956814.47149 21875546.363 89576741.90649 21875544.933
106012532.74649 20173505.537 82607201.93949 20173503.535
125711842.56047 23922167.349 97957288.14148 23922165.931
119238856.33248 22690389.725 92913413.33748 22690387.811
126647445.65347 24100198.242 98686357.86547 24100196.537
115864289.86249 22048234.526 90283862.18149 22048231.774
121423791.97248 23106173.809 94615957.45149 23106172.539
126265507.08247 24027524.736 98388709.67748 24027522.683
109327695.42149 20804367.862 85190428.66449 20804365.462
02 10 3 00 00 30.0000000 0 9 2 3 8 15 17 18 22 27 31
...
PRN02
PRN03
PRN08
PRN15
PRN17 PRN18 PRN22 PRN27 PRN31
Notes: Phase (“L”) records in cycles. Pseudorange (“C”/“P”) records in m. Data records may wrap onto secondary lines, so beware when reading columns. Other common data types are signal-to-noise ratio (“S”) and Doppler shift (“D”) on different frequencies. Nowadays, L5 phase/C5 pseudorange observations becoming more common. L2C and, ultimately, L1C may also be acquired, but may have an impact on simultaneous recording of legacy C/A signal and is currently not recommended (e.g. do not use “+C2” or “-O.obs C2…” teqc options).

## Slide 7: RINEX (3) data format
Must be able to accommodate increased number and complexity of observations from multi-GNSS observations (GPS, GLONASS, Galileo, etc.)
Latest definition at ftp://ftp.igs.org/pub/data/format/rinex303.pdf
Each file type consists of a header section and a data section
Header section contains global information for the entire file and is placed at the beginning of the file.
  Contains header labels in columns 61-80 for each line contained in the header section
  These labels are mandatory and must appear exactly as per format description
RINEX 3 filename convention is longer and more complicated than for RINEX 2, e.g. TG0100USA_R_20150010000_01D_30S_GO.crx.gz
4-character site ID (same as RINEX 2)
Monument and receiver indices
ISO country code
Data source (R = receiver)
First epoch (YYYYDDDhhmm)
File length (01D = 1 day)
Observation interval and type

## Slide 8: Compressing/Uncompressing RINEX
File compression
  “*.zip” files
    Uncompress using “unzip”, “pkzip” or “WinZip”
    See http://www.pkware.com/ or http://www.winzip.com/ , or http://www.7-zip.org/
  “*.??o.Z” (RINEX 2) and “*.rnx.gz” (RINEX 3) files (UNIX compress or gzip)
    e.g., hers0010.02o.Z, TG0100USA_R_20150010000_01D_30S_GO.rnx.gz
    Uncompress using “uncompress”, “gunzip”, “7zip”, “WinZip” or similar
  “*.??d.Z” (RINEX 2) and “*.crx.gz” (RINEX 3) files (Hatanaka compression)
    e.g., hers0010.02d.Z, TG0100USA_R_20150010000_01D_30S_GO.crx.gz
    Need to uncompress as above to get *.??d and *.crx files
    Then need to ‘unHatanaka’ using CRX2RNX from http://sopac.ucsd.edu/dataArchive/hatanaka.html
  Leica Geo Office uncompresses files automatically when using “Internet Download” tool. For manual import you need to uncompress the files manually

## Slide 9: runpkr00 (Trimble raw to dat)
Proprietary software from Trimble
Maintained by UNAVCO nowadays
  http://facility.unavco.org/kb/questions/744/
runpkr00 -g -adeimv <raw file> [dat-file root]
Converts raw data from Trimble receiver to teqc-compatible input “dat”-file
Always use “-g” option separately from other options

## Slide 10: Pre-processing data
Some level of data quality control may be performed prior to any data processing
Utilities are available to perform simple but valuable tests
  The most common example is TEQC (pronounced “tek”)
    Translate, Edit, Quality Check
    Translates common binary formats to RINEX format
    Header editing, windowing, splicing of RINEX data
    Quality check in ‘lite’ mode (no navigation file) or ‘full’ mode (navigation file available)
    Download for free from
  http://www.unavco.org/facility/software/teqc/teqc.html#executables

## Slide 11: Using teqc
Be sure to use correct raw format
  teqc -tr d <Trimble .dat file>
  teqc -ash d <Ashtech B-file, etc.>
Ability to control observations using “-O.obs”
  teqc -O.obs L1L2C1P2 -tr d <Trimble .dat file>
Ability to control header information with other “-O.xxx” options
  teqc -O.o “M. Floyd” -O.obs L1L2C1P2 -tr d <Trimble .dat file>
May create and use a teqc configuration file for consistent information
  teqc -config teqc.cfg -tr d <Trimble .dat file>
Use a script or command line loop to create RINEX files in batch

## Slide 12: TEQC
Quality Control (QC)
  In ‘lite’ mode, teqc doesn’t know anything about the satellite positions
    teqc +qc site1891.02o > teqc.out
    7 files generated; use the -plots switch to prevent all but the summary (‘S’) file being generated
  In ‘full’ mode, additional information is available based on the satellite positions
    teqc +qc –nav site1891.02n site1891.02o > teqc.out
    9 files generated (elevation and azimuth of satellites)
  Full solution if navigation file matches observation file, e.g. site1891.02o and site1891.02n,
    teqc +qc site1891.02o > teqc.out

## Slide 13: Approximate position
Accurate a priori coordinates necessary for good GPS processing
Run teqc to create RINEX observation and (broadcast) navigation files, e.g.
  teqc +nav abcd3650.14n +obs abcd3650.14o -tr d 12343650.dat
Run teqc in qc-mode on observation file with navigation file to get pseudorange-derived estimate of approximate coordinate, e.g.
  teqc +qc -nav abcd3650.14n abcd3650.14o
May also be done using GG’s sh_rx2apr