## Slide 1: Examples using track
M. A. Floyd T. A. Herring Massachusetts Institute of Technology, Cambridge, MA, USA
GNSS Data Processing and Analysis with GAMIT/GLOBK and track UNAVCO Headquarters, Boulder, Colorado, USA 18–22 July 2022
https://geoweb.mit.edu/gg/courses/202207_UNAVCO/
Material from R. W. King, T. A. Herring, M. A. Floyd (MIT) and S. C. McClusky (now at ANU)

## Slide 2: Outline
Kinematic examples
  GNSS seismology
Kinematic/static example
  Rapid deformation
  Episodic and continuous deformation
Static examples
  Short-static occupations
  Deciphering interference
Remember the rule-of-thumb for proportional errors:
  εBL ~ εSV × BL/hSV

## Slide 3: Example 1: GNSS seismology
April 4, 2010 El-Mayor Cucapah earthquake in Baja California
  5-Hz results
  Look later at long baseline processing for these sites
Track results are generated in two steps:
  First solution uses zero process noise except during time of earthquake (long baseline solution)
  Final results generated with fixed ambiguities from first solution read in (-a option)
  Long baseline ambiguity resolution with stochastic site coordinates needs LC estimate which can noisy due to stochastics

## Slide 4: Coseismic offsets
Offsets based on 2-days before and after earthquake
Two days used is reduce leakage of postseismic motions
Red Star is epicenter; blue circle is 60 km (15-20 seconds surface wave speed)

## Slide 5: Zoom around border
Sites near the epicenter.
Blue circle is 60 km radius
Displacements P494 200 mm P496 182 mm P497 97 mm … P491 9 mm

## Slide 6: High-rate GNSS site download
High rate data from these sites downloaded after event.
Most sites are 5-Hz; more distant sites are 1-Hz.
Reference site for high rate positioning
1Hz reference site

## Slide 7: Sites in coseismic region
Sites shown have 5-Hz data for 3-days before and after the earthquake
Examine sequence of sites along US/Mexico border and North
Notes: Sequence in next slides: P494, P496, P500, P066, P473, P472.

## Slide 8: P496

## Slide 9: P494

## Slide 10: P500

## Slide 11: P066

## Slide 12: P473
Notes: Note that this and the next site are similar distances from the epicenter but P742 is along the San Andreas. Also point out the 220-sec arrival

## Slide 13: P742

## Slide 14: Surface wave arrival at P725
P725 is ~600 km from epicenter. This signal common to sites is the arrival at the “reference site”
Notes: Low rate data from distance reference site (with sign flipped)

## Slide 15: Example 2: Rapid deformation (from Ryder et al., 2012)
Two earthquakes within 15 minutes of one another
InSAR shows cumulative deformation with no way to separate events
Epoch-by-epoch (rather than batch) GNSS processing may help...
Ryder et al. (2012), Figure 1
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GNSS processing with track resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 16: Example 2: Rapid deformation (from Ryder et al., 2012)
Selecting fixed site:
CURI is
  Further from the main subduction earthquake
  Outside the deformation zone of the major aftershocks
  Along the nodal (zero deformation) plane of the major aftershocks
Ryder et al. (2012), Figure 3a overlaid in Google Earth

## Slide 17: Example 2: Preliminary run Constrained first runs for ambiguities
Key track commands:
site_stats iloc 10 10 10 0 0 0 lemu 10 10 10 0 0 0 navi 10 10 10 0 0 0
timedep_procns iloc 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 lemu 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 navi 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 iloc 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00 lemu 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00 navi 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00
Second run (updated apr):
site_stats iloc 0.02 0.02 0.02 0 0 0 lemu 0.02 0.02 0.02 0 0 0 navi 0.02 0.02 0.02 0 0 0
timedep_procns iloc 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 lemu 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 navi 1 1 1 2010 03 11 14 40 29 2010 03 11 14 40 30 iloc 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00 lemu 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00 navi 1 1 1 2010 03 11 14 55 59 2010 03 11 14 56 00
site_pos
...
N.B. Remember GNSS is in GPS time, not UTC (need to add leap seconds; axis label is incorrect)
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 18: Example 2: Final run Let the data freely define the noise
Read ambiguities from preliminary, constrained run, e.g grep ‘FINAL’ <sum-file> > track.amb
Key track commands:
site_stats iloc 10 10 10 1 1 1 lemu 10 10 10 1 1 1 navi 10 10 10 1 1 1
timedep_procns iloc 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00 lemu 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00 navi 1 1 1 2010 03 11 14 39 52 2010 03 11 14 40 00 iloc 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00 lemu 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00 navi 1 1 1 2010 03 11 14 55 35 2010 03 11 14 56 00
ambin_file track.amb
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 19: Example 2: track alters perspective
Initial hypothesis
Earthquakes took place on antithetic normal faults in the upper plate of subduction interface
But cGNSS site LEMU experiences opposite vertical motion due to first and second earthquakes
Final conclusion
LEMU is on the hanging wall of first earthquake and footwall of second
Therefore faults must be synthetic normal faults
LEMU
LEMU
Notes: Two large (Mw6.9 and Mw6.7) aftershocks of the 2010-02-27 Mw8.8 Maule (Chile) earthquake occurred within 15 minutes of one another. An initial hypothesis was that they occurred on antithetic normal faults in the hanging wall of the subduction margin, as it extended in the aftermath of the megathrust mainshock, but InSAR data were ambiguous. Epoch-by-epoch GPS processing with TRACK resolved this ambiguity by demonstrating that a site (LEMU) moved in one direction (south-west and down) in the first aftershock and in the opposite direction (north-east and up) in the second. The conclusion is that the aftershocks occurred on synthetic normal faults and LEMU was, coincidentally, in between the ruptured faults, thereby being on the footwall of the first aftershock and on the hanging wall of the second. This is also supported by the InSAR data and modelling.

## Slide 20: A good satellite in cview

## Slide 21: A satellite with some problems cview

## Slide 22: A problematic satellite in cview
Notes: Next slide zooms in between lines.

## Slide 23: A problematic satellite in cview
usr_addbf iloc 17 2010 03 11 14 37 30 usr_addbf iloc 17 2010 03 11 14 51 00
Notes: Lines are at the epochs of two earthquakes. Proximity of cycle slips to epochs of displacements makes it difficult for track to recognize (and resolve) the slips reliably?

## Slide 24: Example 3: Episodic and continuous deformation
GAMIT/GLOBK processing
Process network of available data at nearby sites
Find candidate stable fixed site(s)
Ensure accurate coordinate coordinates for fixed site(s)
track processing
Use network of nearby, bedrock sites as base sites for kinematic processing of ice-flow
One fixed site natural but multiple constrained sites may provide redundancy
Ambiguities must still be resolved correctly

## Slide 25: Building the static network
http://www.unavco.org/data/gps-gnss/data-access-methods/dai2/app/dai2.html

## Slide 26: Ice flow or bedrock?

## Slide 27: Ice flow or bedrock?

## Slide 28: Ice flow or bedrock?

## Slide 29: Ice flow or bedrock?

## Slide 30: Ice flow or bedrock?

## Slide 31: Ice flow or bedrock?
Notes: Site is on roof of Amundsen-Scott South Pole Station. The thick ice sheet beneath moves and the building is capable of being adjusted to stay above accumulating snow.

## Slide 32: Kinematic results using FALL, RAMG and BUMS as fixed sites*
* FALL is the declared fixed site (“F” flag under “obs_file” option); RAMG and BUMS are technically kinematic sites (“K” flag) but are constrained by zero process noise.

## Slide 33: Experiment-specific constraints
Justification
We wish to apply our own temporal constraints (we have moving sites), so let’s be clear on units
Atmosphere is more stable in Antarctica (cold, high pressure)
  Evident in daily GAMIT processing “o”-files
Previous studies show maximum displacement rates of 0.5 m over 30 mins (but loosen temporal constraints for final solution with “ambin_file”)
Key track commands
time_unit second
atm_stats FALL 0.1 0.0001 0 RAMG 0.1 0.0001 0 : : : :
site_stats FALL 10 10 10 0 0 0 RAMG 10 10 10 0 0 0 : : : : : : : LA14 10 10 10 0.1 0.1 0.1 MG01 10 10 10 0.1 0.1 0.1

## Slide 34: Example 4: Short-static occupations
Short spans of data (e.g. 30 minutes) may be processed with GAMIT
Risk of all data being removed during cleaning (autcln) if not high quality
track may be used in “short-static” approach with fixed, continuously recording and well positioned base site
Long session base site with accurate a priori coordinate calculated using GAMIT
Rover
Rover
Rover
Rover

## Slide 35: Example 4: Short-static occupations
Notes: Data from 2000 and 2001 are short-static occupations processed with track. All other data are regular geodetic occupations processed with GAMIT. Note the large outlier (incorrect ambiguity resolution?) at B245 in 2001.

## Slide 36
Sometimes, this happens…
1.2810 m
N
Photographs courtesy of Gareth Funning (University of California, Riverside)

## Slide 37: Example 5(a): Deciphering interference
First, run track with loose constraints to identify probable epoch of disturbance
Update a priori position and re-run track for solution
Re-run teqc with “-e” option to truncate RINEX file at epoch of disturbance so as not to propagate bad data
19:36
local time
Setup
Notes: The tripod at the site pictured in the previous slide (6908, off I-680 south of Cordelia, CA) appears to have been knocked over or collapsed after 2014-08-25T02:36:30Z. This still leaves ~ 5 hours of “untouched” GPS data available for regular static processing, but anything after this epoch ideally should be discarded by truncating the RINEX file to avoid propagation of unusable data.

## Slide 38: Example 5(b): A complex example
20:34
local time
1.0450 m
07:21
local time
~ 9 hrs
???
Notes: This site, 04LF, is within Maxwell Farms Regional Park in Sonoma, California. The path to the right (east) of the site is used as a waiting area for children attending the local school when they get on or off the school bus at the stop in the background. This site is very exposed to public interference and the example here shows how, after 03:34:00 UTC (20:34:00 local time) on 2014-08-31, the site was disturbed. Apparently it is lying on the ground (du = ~ antenna height) a few m away from the mark. Then, after 14:21:30 UTC (07:21:30 local time) the next day, it is approximately (but not exactly) replaced over the mark. Ground truth measurements were taken when the antenna was retrieved showing the replaced tripod to be ~ 70 mm away from the mark on true azimuth ~ 050° at a height of 1.0063 m, 38.7 mm lower than before. While this data may be used with the ground-truthed differential position, it is safest to truncate the data (e.g. in the RINEX file) at 2014-08-31T03:34:00Z.

## Slide 39: References
Ryder, I., A. Rietbrock, K. Kelson, R. Bürgmann, M. Floyd, A. Socquet, C. Vigny and D. Carrizo (2012), Large extensional aftershocks in the continental forearc triggered by the 2010 Maule earthquake, Chile, Geophys. J. Int., 188, 879–890, doi:10.1111/j.1365-246X.2011.05321.x.